## Slide 1: Module 3: Addressing
CompTIA Network+ Guide to Networks, Ninth Edition

## Slide 2: Module Objectives
By the end of this module, you should be able to:
1. Work with MAC addresses
2. Configure TCP/IP settings on a computer, including IP address, subnet mask, default gateway, and DNS servers
3. Identify the ports of several common network protocols
4. Describe domain names and the name resolution process
5. Use command-line tools to troubleshoot common network problems

## Slide 3: Addressing Overview
There are four addressing methods:
  Data link layer MAC (Media Access Control) address is 48 bits, written as six hex numbers separated by colons
    It is also called a physical address
    MAC addresses are embedded on every NIC in the world
  Network layer IP (Internet Address) address can be used to find any computer in the world
    IPv4 addresses have 32 bits and are written as four decimal numbers called octets
    IPv6 addresses have 128 bits and are written as eight blocks of hexadecimal number
  Transport layer port numbers are used to find applications
  Application layer FQDNs, computer names, and host names
    Fully qualified domain name (FQDN) – a unique character-based name

## Slide 4: MAC Addresses (1 of 2)
Traditional MAC addresses contain two parts
  The first 24 bits are known as the OUI (Organizationally Unique Identifier) or manufacturer-ID
    This part is assigned by the IEEE
  The last 24 bits make up the extension identifier or device ID
    Manufacturer’s assign each NIC a unique device ID
Switches use MAC addresses to identify devices on the local area network

## Slide 5: MAC Addresses (2 of 2)
Figure 3-3 The switch learns the sending device’s MAC address

## Slide 6: IP Addresses
Static IP addresses are assigned manually by the network administrator
Dynamic IP addresses are automatically assigned by a DHCP server
  You’ll learn more about DHCP later in the chapter
There are two types of IP addresses:
  IPv4 is a 32-bit address
  IPv6 is a 128-bit address

## Slide 7: IPv4 Addresses (1 of 4)
A 32-bit IPv4 address is organized into four groups of 8 bits each (known as octets)
  Each of the four octets can be any number from 0 to 255
  Some IP addresses are reserved
Example of an IPv4 address: 72.56.105.12
Classful addressing
  The dividing line between the network and host portions is determined by the numerical range the IP address falls in
Classful IPv4 addresses are divided into five classes:
  Class A, Class B, Class C, Class D, and Class E

## Slide 8: IPv4 Addresses (2 of 4)
Class A, B, and C licensed IP addresses are available for use on the Internet
  These are called public IP addresses
A company can use private IP addresses on its private networks
The IANA recommends the following IP addresses be used for private networks:
  10.0.0.0 through 10.255.255.255
  172.16.0.0 through 172.31.255.255
  192.168.0.0 through 192.168.255.255
Classless addressing allows the dividing line between network and host portions to fall anywhere along the string of binary bits in an IP address
CIDR (Classless Interdomain Routing) notation takes the network ID or a host’s IP address and follows it with a forward slash (/) followed by the number of bits that are used for the network ID

## Slide 9: IPv4 Addresses (3 of 4)
Network Address Translation (NAT) is a technique designed to conserve public IP addresses needed by a network
Address translation is a process where a gateway device substitutes the private IP addresses with its own public address
  When these computers need access to other networks or Internet
Port Address Translation (PAT) is the process of assigning a TCP port number to each ongoing session between a local host and Internet host
Two variations of NAT to be aware of:
  SNAT (Source Network Address Translation) - the gateway assigns the same public IP address to a host each time it makes a request to access the Internet
  DNAT (Dynamic Network Address Translation) - the gateway has a pool of public address that it is free to assign to a local host when it makes a request to access the Internet

## Slide 10: IPv4 Addresses (4 of 4)
Figure 3-12 PAT (Port Address Translation)

## Slide 11: IPv6 Addresses (1 of 2)
An IPv6 address has 128 bits written as eight blocks of hexadecimal numbers separated by colons
  Ex: 2001:0000:0B80:0000:0000:00D3:9C5A:00CC
  Each block is 16 bits
  Leading zeros in a four-character hex block can be eliminated
  If blocks contain all zeroes, they can be written as double colons (::), only one set of double colons is used in an IP address
  Therefore, above example can be written two ways:
    2001::B80:0000:0000:D3:9C5A:CC
    2001:0000:B80::D3:9C5A:CC (this is the preferred method because it contains the fewest zeroes)

## Slide 12: IPv6 Addresses (2 of 2)
IPv6 terminology:
  A link (sometimes called local link) is any LAN bounded by routers
  Neighbors are two or more nodes on the same link
  Dual stacked is when a network is configured to use both IPv4 and IPv6
  Tunneling is a method used by IPv6 to transport IPv6 packets through or over an IPv4 network
  Interface ID is the last 64 bits or four blocks of an IPv6 address that identify the interface

## Slide 13: Types of IPv6 Addresses (1 of 4)
Unicast address - specifies a single node on a network
  Global address can be routed on the Internet
  Link local address can be used for communicating with nodes in the same link
  Loopback address can be used to test that an interface and supporting protocol stack are functioning properly
Multicast address – delivers packets to all nodes on a network
Anycast address - can identify multiple destinations, with packets delivered to the closest destination

## Slide 14: Types of IPv6 Addresses (2 of 4)
Figure 3-16 Three types of IPv6 addresses

## Slide 15: Types of IPv6 Addresses (3 of 4)
Figure 3-18 The ipconfig command shows IPv4 and IPv6 addresses assigned to this computer

## Slide 16: Types of IPv6 Addresses (4 of 4)
IPv6 autoconfiguration
  IPv6 addressing is designed so that a computer can autoconfigure its own link local IP address
  This process is called SLAAC (stateless address autoconfiguration)
Step 1 - The computer creates its IPv6 address
  It uses FE80::/64 as the first 64 bits (called prefix)
  The last 64 bits are generated from the network adapter’s MAC address
Step 2 - The computer checks to make sure its IP address is unique on the network
Step 3 - The computer asks if a router on the network can provide configuration information
  This message is called an RS (router solicitation) message

## Slide 17: Knowledge Check Activity 3-1
Which of the following IPv4 addresses is a public IP address?
10.0.2.14
172.16.156.254
192.168.72.73
64.233.177.189
Notes: Instructions:
Net+: you will choose two of the Self-Check questions from each module and re-use them for Knowledge Check Activities. The activity numbers change based on the module you are in. (e.g., 1-1 and 1-2; 2-1 and 2-2; etc.) The CM will provide you with the final page proofs from the textbook.

## Slide 18: Knowledge Check Activity 3-1: Answer
Which of the following IPv4 addresses is a public IP address?
Answer: d. 64.233.177.189
IP addresses within the ranges of 10.0.0.0 through 10.255.255.255, 172.16.0.0 through 172.31.255.255, and 192.168.0.0 through 192.168.255.255 are RFC1918, or private, IP addresses. The address 64.233.177.189 is a public IP address.
Notes: Include only the question and the correct answer on the slide or include only the correct answer on the slide. The CM will provide you with the Solution and Answer Guide for the correct answers.

## Slide 19: Ports and Sockets (1 of 2)
A port is a number assigned to a process that can receive data
  Port numbers ensure data is transmitted to the correct process among multiple processes running on a single device
A socket consists of host’s IP address and the port number of an application running on the host
  A colon separates the two values
  Example - 10.43.3.87:23
Port numbers are divided into three types:
  Well-known ports - 0 to 1023
  Registered ports - 1024 to 49151
  Dynamic and private ports - 49152 to 65535

## Slide 20: Ports and Sockets (2 of 2)
Figure 3-19 A virtual connection for the Telnet service

## Slide 21: Domain Names and DNS (1 of 2)
Character-based names are easier to remember than numeric IP addresses
A URL (uniform resource locator) is an addressing scheme that identifies where to find a particular resource on a network
Last part of an FQDN is called the top-level domain (TLD)
Domain names must be registered with an Internet naming authority that works on behalf of ICANN
  ICANN restricts what type of hosts can be associated with .arpa, .mil, .int, .edu, and .gov
Name resolution is the process of discovering the IP address of a host when you know the FQDN

## Slide 22: Domain Names and DNS (2 of 2)
DNS is an Application layer client-server system of computers and databases made up of these elements:
  Namespace - the entire collection of computer names and their associated IP addresses stored in databases on DNS name servers around the globe
  Name servers - hold databases, which are organized in a hierarchical structure
  Resolvers - a DNS client that requests information from DNS name servers

## Slide 23: Namespace Databases
Each organization that provides host services is responsible for providing and maintaining its own DNS authoritative servers for public access
  An authoritative name server is the authority on computer names and their IP addresses for computers in their domains
The domains that the organization is responsible for managing are called a DNS zone

## Slide 24: Name Servers (1 of 4)
Four common types of DNS servers:
  Primary DNS server – the authoritative name server for the organization
    Holds the authoritative DNS database for the organization’s zones
  Secondary DNS server – backup authoritative name server for the organization
  Caching DNS server – accesses the public DNS data and caches the DNS information it collects
  Forwarding DNS server – receives queries from local clients but doesn’t work to resolve the queries
Any of these DNS server types can co-exist on the same machine
DNS name servers are organized in a hierarchical structure
At the root level, 13 clusters of root DNS servers hold information used to locate top-level domain (TLD) servers

## Slide 25: Name Servers (2 of 4)
Figure 3-21 Hierarchy of name servers

## Slide 26: Name Servers (3 of 4)
Figure 3-22 Queries for name resolution of www.mdc.edu

## Slide 27: Name Servers (4 of 4)
Ways the resolution process can get more complex:
  A caching server typically is not the same machine as the authoritative server
    The caching server exists only to resolve names for its own local clients
  Name servers within a company might not have access to root servers
  A TLD name server might be aware of an intermediate name server rather than the authoritative name server
Two types of DNS requests:
  Recursive lookup – a query that demands a resolution or the answer “It can’t be found”
  Iterative lookup – a query where the local server issues queries to other servers
    Other servers only provide information if they have it
    Do not demand a resolution

## Slide 28: Resource Records in a DNS Database
Several types of records, called resource records are kept in a DNS database:
  SOA (start of authority) record – gives information about the zone
  A (address) record – stores the name-to-address mapping for a host
  AAAA (address) record – holds the name-to-address mapping, the IP address is an IPv6 type IP address
  CNAME (canonical Name) record – holds alternative names for a host
  PTR (pointer) record – used for reverse lookups
  NS (name Server) record – indicates the authoritative name server for a domain
  MX (mail exchanger) record – identifies a mail server and is used for email traffic
  SRV (service) record – identifies the hostname and port of a computer that hosts a specific network services besides email
  TXT (text) record – holds any type of free-form text

## Slide 29: DNS Server Software
BIND (Berkeley Internet Name Domain) is the most popular DNS server software
  Open source - the term for software whose code is publicly available for use and modification
Microsoft DNS Server is a built-in DNS service in the Windows Server OS
Windows Server is capable of split-brain or split-horizon deployment, which is used to handle internal clients and external clients

## Slide 30: Troubleshooting Address Problems
Figure 3-24 Event Viewer provided the diagnosis of a printer problem and recommended steps to fix the problem

## Slide 31: Troubleshooting Tools (1 of 8)
Command-line tools are a great resource to troubleshoot network problems
ping (Packet Internet Groper) utility is used to verify that TCP/IP is:
  Installed
  Bound to the NIC
  Configured correctly
  Communicating with the network
The ping utility sends out a signal called an echo request to another device (request for a response)
  The other computer responds in the form of an echo reply
ICMP (Internet Control Message Protocol) is the protocol used by the echo request/reply to carry error messages and information about the network

## Slide 32: Troubleshooting Tools (2 of 8)
IPv6 networks use a version of ICMP called ICMPv6
  ping6 – on Linux computers running IPv6, use ping6 to verify whether an IPv6 host is available
  ping -6 – on Windows computers, use ping with the -6 switch to verify connectivity on IPv6 networks
For the ping6 and ping -6 commands to work over the Internet, you must have access to the IPv6 Internet

## Slide 33: Troubleshooting Tools (3 of 8)
The ipconfig command shows current TCP/IP addressing and domain name information on a Windows computer
  Use ipconfig/all to see a more complete summary of TCP/IP addressing information

## Slide 34: Troubleshooting Tools (4 of 8)
Figure 3-29 ipconfig /all gives more information than ipconfig by itself

## Slide 35: Troubleshooting Tools (5 of 8)
Use the ip utility to view and manage TCP/IP settings
The ip utility is only available on UNIX and Linux systems
Any ip commands that change the state of a link require elevated privileges
  This is accomplished by logging in as the root user or by temporarily elevating the current user's privileges with the sudo (superuser do) command
ifconfig is a similar utility used to view and manage TCP/IP settings
If your Linux or UNIX system provides a GUI
  Open a shell prompt, then type ifconfig

## Slide 36: Troubleshooting Tools (6 of 8)
Figure 3-32 Use hostname to view or change a device’s host name

## Slide 37: Troubleshooting Tools (7 of 8)
The nslookup (name space lookup) utility allows you to query the DNS database from any computer on a network
  To find the host name of a device by specifying its IP address, or vice versa
  It is useful for verifying a host is configured correctly or for troubleshooting DNS resolution problems
Reverse DNS lookup - to find the host name of a device whose IP address you know
  nslookup 69.23.208.74
The nslookup utility is available in two modes:
  Interactive - to test multiple DNS servers at one time
  Noninteractive - test a single DNS server
You can change DNS servers from within interactive mode with the server subcommand and specifying the IP address of the new DNS server
To exit nslookup’s interactive mode, enter exit

## Slide 38: Troubleshooting Tools (8 of 8)
The dig (domain information groper) utility is available on Linux and macOS
  Provides more detailed information than nslookup and uses more reliable sources of information to output its results
Use dig to query DNS nameservers for information about host addresses and other DNS records
An IP scanner can be used to gather information about all devices connected to a network

## Slide 39: Common Network Issues (1 of 2)
Incorrect time
  Check a domain computer’s time source from a Command Prompt window by entering w32tm /query /source
DHCP Issues
  If you are getting DHCP errors or if multiple clients are having trouble connecting to the network, try the following:
    Check the settings on your DHCP server
    Make sure the DHCP scope is large enough to account for the number of clients the network must support
  Consider implementing a shorter lease time on larger networks

## Slide 40: Common Network Issues (2 of 2)
Network Connection Configuration Issues
  Common configuration errors:
    Incorrect IP address
    Duplicate IP address
    Incorrect subnet mask
    Incorrect gateway
    Incorrect DNS or DNS issues
  When a computer is struggling to establish a network connection
    Check its TCP/IP configuration settings
  If the computer is not obtaining an IP address and related information from a DHCP server
    Static settings might be using the wrong information
    Try switching to DHCP

## Slide 41: Knowledge Check Activity 3-2
What protocol does ping use?
HTTP
ICMP
DHCP
FTP
Notes: Instructions:
Net+: you will choose two of the Self-Check questions from each module and re-use them for Knowledge Check Activities. The activity numbers change based on the module you are in. (e.g., 1-1 and 1-2; 2-1 and 2-2; etc.) The CM will provide you with the final page proofs from the textbook.

## Slide 42: Knowledge Check Activity 3-2: Answer
What protocol does ping use?
Answer: b. ICMP
The protocol used by the ping echo request and echo reply is ICMP (Internet Control Message Protocol), a lightweight protocol used to carry error messages and information about a network.
Notes: Include only the question and the correct answer on the slide or include only the correct answer on the slide. The CM will provide you with the Solution and Answer Guide for the correct answers.

## Slide 43: Summary
Now that the lesson has ended, you should be able to:
Work with MAC addresses
Configure TCP/IP settings on a computer, including IP address, subnet mask, default gateway, and DNS servers
Identify the ports of several common network protocols
Describe domain names and the name resolution process
Use command-line tools to troubleshoot common network problems