## Slide 1: Module 4: Protocols
CompTIA Network+ Guide to Networks, Ninth Edition

## Slide 2: Module Objectives
By the end of this module, you should be able to:
1. Describe the functions of core TCP/IP protocols
2. Identify how each protocol’s information is formatted in a TCP/IP message
3. Secure network connections using encryption protocols
4. Configure remote access connections between devices
5. Employ various TCP/IP utilities for network discovery and troubleshooting

## Slide 3: TCP/IP Core Protocols (1 of 3)
TCP/IP is a suite of protocols including:
  TCP, IP (IPv4 and IPv6), UDP, ARP, and many others
TCP/IP protocols add a header to data inherited from the layer above it
Layers 7, 6, and 5 - Data and instructions, known as payload, are generated by applications running on source host
Layer 4 – A Transport Layer protocol, usually TCP or UDP, adds a header to the payload
  Includes a port number to identify the receiving app
Layer 3 - Network layer adds it own header and becomes a packet
Layer 2 - packet is passed to Data Link layer on NIC, which encapsulates data with its own header and trailer, creating a frame
Layer 1 - Physical layer on the NIC receives the frame and places the transmission on the network

## Slide 4: TCP/IP Core Protocols (2 of 3)
Figure 4-1 Each layer adds its own data and addresses its transmission to the corresponding layer in the destination device

## Slide 5: TCP/IP Core Protocols (3 of 3)
The receiving host decapsulates the message at each layer in reverse order and presents payload to the receiving applications
  In transit, transmissions might pass through a number of connectivity devices
Connectivity devices are specialized devices that allow two or more networks or multiple parts of one network to connect and exchange data
  Known by the highest OSI layer they read and process

## Slide 6: TCP (Transmission Control Protocol) (1 of 4)
TCP operates in the transport layer of OSI model
Three characteristics of TCP:
  Connection-oriented - TCP ensures that a connection or session is established by using a three-step process called a three-way handshake
  Sequencing and checksums - TCP sends a character string called a checksum that is checked by the destination host along with a sequence number for each segment
  Flow control - gauges rate of transmission based on how quickly recipient can accept data

## Slide 7: TCP (Transmission Control Protocol) (2 of 4)
Figure 4-3 A TCP segment

## Slide 8: TCP (Transmission Control Protocol) (3 of 4)
The TCP three-way handshake establishes a session before TCP transmits actual data
  Three transmissions are sent before data transmission:
    Step 1 – a request for a connection (SYN)
    Step 2 – a response to the request (SYN/ACK)
    Step 3 – a connection is established (ACK)
  After the three initial messages, the payload or data is sent
  Sequence numbers will be increased by the number of bits included in each received segment
    Confirms the correct length of message was received

## Slide 9: TCP (Transmission Control Protocol) (4 of 4)
Figure 4-4 The three-way handshake process establishes a TCP session

## Slide 10: UDP (User Datagram Protocol)
UDP is an unreliable, connectionless protocol
  No three-way handshake is performed
  UDP does not guarantee delivery of data
UDP provides no error checking, sequencing, or flow control
  This makes UDP more efficient than TCP
Useful for live audio or video transmissions over the Internet
Also more efficient for carrying messages that fit within one data packet
A UDP header contains only four fields: Source port, Destination port, Length, and Checksum
  Use of Checksum field in UDP is optional in IPv4, but required in IPv6

## Slide 11: IP (Internet Protocol) (1 of 3)
IP operates at the network layer of the OSI model
  It specifies where data should be delivered
  Identifies the data’s source and destination IP addresses
IP enables TCP/IP to internetwork
  To traverse more than one LAN segment and more than one type of network through a router
IP is an unreliable, connectionless protocol
  That means that IP does not guarantee delivery of data and no session is established before data is transmitted
IP depends on TCP to ensure messages are put back together in the right order and to ensure each message reaches the correct application on the receiving host

## Slide 12: IP (Internet Protocol) (2 of 3)
Figure 4-7 An IPv4 packet

## Slide 13: IP (Internet Protocol) (3 of 3)
IPv6 Packets
  IPv6 uses a different packet format than IPv4
  IPv6 can accommodate the much longer IPv6 addresses
  There is no Fragment offset field
    IPv6 hosts adjust their packet sizes to fit the requirements of the network before sending IPv6 messages

## Slide 14: ICMP (Internet Control Message Protocol)
ICMP is a core network layer protocol that reports on the success or failure of data delivery
ICMP can indicate the following:
  When part of a network is congested
  When data fails to reach its destination
  When data has been discarded because the allotted TTL has expired
ICMP announces transmission failures to the sender but does not correct errors it detects
It provides critical information for troubleshooting network problems
ICMPv6 on IPv6 networks performs the functions of ICMP and ARP on IPv4 networks

## Slide 15: ARP (Address Resolution Protocol) on IPv4 Networks (1 of 2)
ARP works in conjunction with IPv4 to discover the MAC address of a host or node on the local network
  And to maintain a database that maps IP addresses to MAC addresses on the local network
ARP is a Layer 2 protocol that uses IP in Layer 3 and relies on broadcasting
  Operates only within its local network
ARP table is the database of IP-to-MAC address mappings
An ARP table can contain two types of entries:
  Dynamic - created when a client makes an ARP request that could not be satisfied by data already in the ARP table
  Static - those someone entered manually using the ARP utility (arp command)
To view a Window’s workstation’s ARP table, enter the command:
  arp -a

## Slide 16: ARP (Address Resolution Protocol) on IPv4 Networks (2 of 2)
Figure 4-13 The arp –a command lists devices on the network

## Slide 17: NDP (Neighbor Discovery Protocol)
IPv6 devices learn about other devices on their networks through a process called neighbor discovery
NDP (Neighbor Discovery Protocol) information carried in ICMPv6 messages automatically detects neighboring devices and automatically adjusts when nodes fail or are removed
NDP offers several ICMPv6 message types:
  RA (router advertisement)
  RS (router solicitation)
  Redirect
  NS (neighbor solicitation)
  NA (neighbor advertisement)

## Slide 18: Ethernet (1 of 2)
Ethernet is the most important data link layer standard
  It is capable of running on a variety of network media
  Ethernet offers excellent throughput at a reasonable cost
  It is the most popular network technology used on modern LANs
Ethernet II is the current standard
Ethernet adds both a header and a trailer to the payload
  This creates a frame around the payload
The header and FCS make up the 18-byte “frame” around the data
The data portion of an Ethernet frame may contain from 46 to 1500 bytes
MTU (maximum transmission unit) is the largest size that routers in a message’s path will allow at the Network Layer

## Slide 19: Ethernet (2 of 2)
Figure 4-14 Ethernet II frame

## Slide 20: Knowledge Check Activity 4-1
Which protocol’s header includes the source MAC address?
Ethernet
UDP
IP
TCP
Notes: Instructions:
Net+: you will choose two of the Self-Check questions from each module and re-use them for Knowledge Check Activities. The activity numbers change based on the module you are in. (e.g., 1-1 and 1-2; 2-1 and 2-2; etc.) The CM will provide you with the final page proofs from the textbook.

## Slide 21: Knowledge Check Activity 4-1: Answer
Which protocol’s header includes the source MAC address?
Answer: a. Ethernet
Ethernet encapsulates data with a header and trailer, creating a frame. This frame includes the MAC address of the sender.
Notes: Include only the question and the correct answer on the slide or include only the correct answer on the slide. The CM will provide you with the Solution and Answer Guide for the correct answers.

## Slide 22: Encryption Protocols
Encryption protocols use a mathematical code, called a cipher, to scramble data into a format that can be read only by reversing the cipher
The purpose of encryption is to keep information private
Encryption methods are primarily evaluated by three benchmarks:
  Confidentiality
  Integrity
  Availability
The principles above form the standard security model called the CIA triad

## Slide 23: Key Encryption (1 of 2)
A key is a random string of characters woven into original data’s bits
  It generates unique data block called ciphertext
  The key is created according to a specific set of rules (algorithms)
Key encryption can be separated into two categories:
  Private key encryption
  Public key encryption

## Slide 24: Key Encryption (2 of 2)
Figure 4-15 Private key encryption uses only one key, which must be securely communicated between sender and receiver, while public key encryption relies on a second, public key that can safely be obtained by anyone

## Slide 25: IPsec (Internet Protocol Security)
IPsec is an encryption protocol suite that defines rules for encryption, authentication, and key management for TCP/IP transmissions
IPsec creates secure connections in five steps:
  1. IPsec initiation
  2. Key management
  3. Security negotiations
  4. Data transfer
  5. Termination
Operates in two modes:
  Transport mode
  Tunnel mode

## Slide 26: SSL (Secure Sockets Layer) and TLS (Transport Layer Security)
Both SSL and TLS are methods of encrypting TCP/IP transmissions
Both protocols work side by side and are widely known as SSL/TLS or TLS/SSL
When a client and server establish a SSL/TLS connection, they establish a unique session which is an association between client and server
  The session is defined by an agreement on a specific set of encryption techniques
  A session is created by an SSL handshake protocol
The handshake protocol allows client and server to authenticate
  This handshake is similar to a TCP three-way handshake

## Slide 27: Remote Access Protocols
Remote access is a service that allows a client to connect with and log on to a server, LAN, or WAN in a different geographical location
Remote access requires a type of RAS (remote access server)
There are two types of remote access servers:
  Dedicated devices
  Software running on a server
Types of remote access include:
  Remote file access
  Terminal emulation, also called remote virtual computing
  VPN (virtual private network)

## Slide 28: Remote File Access
FTP (File Transfer Protocol) provides remote file access
Three related technologies include the following:
  FTPS (FTP Secure or FTP over SSL) offers an added layer of protection for FTP using SSL/TLS
  SFTP (Secure FTP) is a file-transfer version SSH that include encryption and authentication for transferring files
  TFTP (Trivial FTP) is a simple protocol similar to FTP except that it includes no authentication or security for transferring files

## Slide 29: Terminal Emulation (1 of 4)
A terminal emulator is software that allows a user on one computer (client) to control another computer (host or server)
Examples of command-line software:
  Telnet and SSH
Examples of GUI-based software:
  Remote Desktop for Windows
  join.me
  VNC
  Team Viewer

## Slide 30: Terminal Emulation (2 of 4)
Telnet is a terminal emulation utility that allows an administrator or other user to control a computer remotely
  It provides little security for establishing a connection (poor authentication)
  It provides no security for transmitting data (no encryption)
SSH (Secure Shell) is a collection of protocols that provides for secure authentication and encryption
  Guards against a number of security threats
    Unauthorized access to a host
    IP spoofing
    Interception of data in transit
    DNS spoofing
  Secure connection requires SSH running on both client and server
  Allows for password authentication using public and private key generation

## Slide 31: Terminal Emulation (3 of 4)
Figure 4-20 On a Windows computer, use an app like PuTTY to create an SSH connection to another computer

## Slide 32: Terminal Emulation (4 of 4)
RDP (Remote Desktop Protocol) is a Microsoft proprietary protocol used to connect to and control a remote computer
VNC (Virtual Network Computing) uses the cross-platform protocol RFB (remote frame buffer) to remotely control a workstation or server
  VNC is open source so many companies have developed their own software that can:
    Run OSes on client computers
    Remotely access computers, tablets, and smartphones
    Remotely control media equipment and surveillance systems
Out-of-band management relies on a dedicated connection between the network administrator’s computer and each network device
  A remote management card is attached to the network device’s console port
  A single device, such as a console server or console router, provides centralized management of all linked devices

## Slide 33: VPNs (Virtual Private Networks) (1 of 4)
A VPN is a network connection encrypted from end to end that creates a private connection to a remote network
  A VPN is sometimes referred to as a tunnel
VPNs can be classified according to three models:
  Site-to-site VPN
  Client-to-site VPN
    Also called host-to-site VPN or remote-access VPN
  Host-to-host VPN

## Slide 34: VPNs (Virtual Private Networks) (2 of 4)
To ensure VPNs can carry all types of data securely, special VPN protocols encapsulate higher-layer protocols in a process known as tunneling
Many VPN tunneling protocols operate at the data link layer to encapsulate the VPN frame into a network layer packet
Some VPN tunneling protocols work at Layer 3, which enables additional features and options
Most tunneling protocols rely on an additional encryption protocol to provide data security
Common VPN tunneling protocols include:
  L2TP (Layer 2 Tunneling Protocol)
  GRE (Generic Routing Encapsulation)
  Open VPN
  IKEv2

## Slide 35: VPNs (Virtual Private Networks) (3 of 4)
Figure 4-25 The VPN frame, such as GRE or L2TP, is encapsulated inside the network layer packet

## Slide 36: VPNs (Virtual Private Networks) (4 of 4)
Cisco developed a proprietary protocol called mGRE (multipoint GRE) that allows the configuration of multiple tunnel destinations on a single interface
A type of enterprise VPN using Cisco devices is called DMVPN (Dynamic Multipoint VPN)
DMVPN dynamically creates VPN tunnels between branch locations as needed rather than requiring constant, static tunnels for site-to-site connections

## Slide 37: Remote Access Policies
Common requirements of a good remote access policy:
  Remote access devices must be up to date with patches, anti-malware software, and a firewall
  Device access must be controlled by a strong password or biometric measures
  Passwords must be strong and must be changed periodically
  The device’s internal and external storage devices must be encrypted
  Company and customer data must be kept secure
  The loss or theft of any devices used for remote access must be reported immediately
  Encrypted VPN software must be used to remotely access company network resources
  While remotely connected to the company network, the device must not be connected to the open Internet or any other network not fully owned or controlled by the employee
  Remote sessions must be terminated when not in use

## Slide 38: Troubleshooting Network Issues (1 of 3)
netstat displays TCP/IP statistics and details about TCP/IP components/connections on a host
  Information that can be obtained from the netstat command includes:
    The port on which a TCP/IP service is running
    Which network connections are currently established for a client
    How many messages have been handled by an interface since it was activated
    How many data errors have occurred on a particular network interface
tracert or traceroute
  Windows tracert utility uses ICMP echo requests to trace the path from one networked node to another, identifying all intermediate hops between the nodes
  Linux, UNIX, and OS X system use the traceroute utility to send UDP messages to a random port on the destination node (concept is the same as tracert)

## Slide 39: Troubleshooting Network Issues (2 of 3)
Figure 4-27 The traceroute utility uses error messages from routers to map nodes on a route

## Slide 40: Troubleshooting Network Issues (3 of 3)
tcpdump is a free, command-line packet sniffer that runs on Linux and other Unix OSs
  It captures traffic that crosses a computer’s network interface
  Output can be saved to a file that you can filter or play back
  You must either use the sudo command or log in as root to access tcpdump

## Slide 41: Solving Common Network Problems (1 of 2)
Duplicate MAC Addresses
  Two devices on the same network with the same MAC address is a problem
  MAC addresses can be impersonated, which is a security risk called spoofing
  It happens most often when managing multiple virtual devices on a large network
  Most switches will detect the problem and produce helpful error messages
    Then it’s a matter of tracking down which virtual devices have the same MAC address and update each device’s configuration

## Slide 42: Solving Common Network Problems (2 of 2)
Hardware Failure - when a router, switch, NIC, or other hardware goes down:
  Use tracert or traceroute to track down malfunctioning routers and other devices on larger networks
  Get more accurate trace feedback on a questionable router by targeting a node on the other side of that router, rather than aiming for that router itself
  Use ping to test for network connectivity

## Slide 43: Knowledge Check Activity 4-2
What protocol must be allowed through a firewall for tracert to work correctly?
SSH
NDP
ICMP
TLS
Notes: Instructions:
Net+: you will choose two of the Self-Check questions from each module and re-use them for Knowledge Check Activities. The activity numbers change based on the module you are in. (e.g., 1-1 and 1-2; 2-1 and 2-2; etc.) The CM will provide you with the final page proofs from the textbook.

## Slide 44: Knowledge Check Activity 4-2: Answer
What protocol must be allowed through a firewall for tracert to work correctly?
Answer: c. ICMP
The Windows tracert utility sends an ICMP (Internet Control Message Protocol) echo request to the destination node and listens for an ICMP echo reply from that node.
Notes: Include only the question and the correct answer on the slide or include only the correct answer on the slide. The CM will provide you with the Solution and Answer Guide for the correct answers.

## Slide 45: Summary
Now that the lesson has ended, you should be able to:
Describe the functions of core TCP/IP protocols
Identify how each protocol’s information is formatted in a TCP/IP message
Secure network connections using encryption protocols
Configure remote access connections between devices
Employ various TCP/IP utilities for network discovery and troubleshooting